## Slide 1
1/15
QGIS + AI
Automate Your GIS Workflow
Site Selection Analysis with PyQGIS & Python
From 4,708 buildings to 9 suitable sites — in one command

## Slide 2
2/15
❌ The Problem
🕐 Manual site selection takes 4+ hours
🔄 Buffer → Clip → Select → Export → Repeat
❌ Error-prone — miss a step, wrong answer
📋 Not reproducible — can you redo it next month?
💰 Expensive — billable hours for repetitive tasks
🧠 Your skill is analysis, not clicking buttons
🎯 The Task
1. Area between 800–1,200 m²
2. Within 1 km of a school
3. NOT within 100 m of a highway
4. NOT within 300 m of a river
5. Inside a residential urban zone
6. Calculate population estimate
QGIS + AI Automation Workshop · github.com/your-repo

## Slide 3
3/15
✅ The Solution
⚡ QGIS Headless Mode + PyQGIS = Automation
🔧 Same algorithms you know — just scripted
📦 800+ processing algorithms available
🔁 Repeatable · Auditable · Shareable
🐍 One Python script replaces hours of clicking
🌍 Publish to web dashboard automatically
🐍 One Command
python3 demo.py ┌──────────────────────────┐ │ 4,708 buildings │ │ → 28 (area filter) │ │ → 22 (school zone) │ │ → 21 (no highway) │ │ → 9 (no river) │ │ → 9 (urban zone) ✅ │ └──────────────────────────┘
QGIS + AI Automation Workshop · github.com/your-repo

## Slide 4
4/15
🗂️ The Dataset
🏘️ Buildings
4,708 features
(Polygon)
🏫 Schools
4 features
(Polygon)
🛣️ Roads
717 features
(Line)
🌊 Rivers
19 features
(Line)
🏙️ Urban Zones
6 features
(Polygon)
💧 Water
37 features
(Polygon)
🍽️ Restaurants
11 features
(Polygon)
📍 Cape Agulhas, South Africa · CRS: EPSG:4326 / EPSG:32733 · Dataset: QGIS Training Manual · Data: © OpenStreetMap (ODbL)
QGIS + AI Automation Workshop · github.com/your-repo

## Slide 5
5/15
📋 The Selection Criteria
1
Area 800 – 1,200 m²
Algorithm: native:extractbyexpression
Filter buildings by size
2
Within 1,000 m of school
Algorithm: native:buffer → extractbylocation
Buffer schools, select intersect
3
NOT within 100 m of highway
Algorithm: native:buffer → extractbylocation
Buffer highways, select disjoint
4
NOT within 300 m of river
Algorithm: native:buffer → extractbylocation
Buffer rivers, select disjoint
5
Inside urban (residential) zone
Algorithm: native:extractbylocation
Select intersect with urban
6
Calculate population estimate
Algorithm: native:fieldcalculator
Area / 30 = people per building
QGIS + AI Automation Workshop · github.com/your-repo

## Slide 6
6/15
⚙️ The Processing Pipeline
Load GeoPackage Layers
Reproject to UTM 33S
Filter by Area 800-1200m²
Buffer Schools 1,000m → Select
Buffer Highways 100m → Exclude
Buffer Rivers 300m → Exclude
Clip to Urban Zones
Calculate Population
Export Dashboard
PyQGIS Processing Algorithms (native:*) — same tools as the QGIS toolbox, automated via Python
📥 Input: 4,708 buildings
7 raw GeoPackage layers + satellite imagery
📤 Output: 9 suitable sites
Interactive dashboard · GeoJSON PDF report · Population estimate
QGIS + AI Automation Workshop · github.com/your-repo

## Slide 7
7/15
📊 The Filter Cascade
Total Buildings
4708
Area 800-1200 m²
28
Within 1 km of School
22
Not Near Highway
21
Not Near River
9
In Urban Zone ✅
9
QGIS + AI Automation Workshop · github.com/your-repo

## Slide 8
8/15
🖥️ The Showcase Dashboard
📊 Stats Cards
Filtering cascade at a glance — 4,708 → 9
🗺️ Interactive Map
Green = suitable sites · Red = highway exclusion · Blue = school zone
📉 Filter Funnel
Visual bar chart of each selection step
📋 Data Table
Searchable, sortable, paginated site register
📥 Export CSV
One-click download of the sites register
🌐 Export GeoJSON
One-click download for QGIS/PostGIS
📄 Print / PDF
Ctrl+P → Save as PDF — professional report ready
💡 Open phase3_dashboard.html in any browser — no installation needed
QGIS + AI Automation Workshop · github.com/your-repo

## Slide 9
9/15
🎬 Live Demo
python3 demo.py
1️⃣ Open terminal → type python3 demo.py
2️⃣ Press Enter → watch all 7 layers load
3️⃣ Watch the cascade: 4,708 → 9
4️⃣ Dashboard opens automatically in browser
5️⃣ Explore data table, export options, PDF report
QGIS + AI Automation Workshop · github.com/your-repo

## Slide 10
10/15
🐍 How It Works — PyQGIS Code
Same QGIS toolbox tools — automated in 10 lines of Python
# 1. Reproject to UTM 33S for meter-based analysis buildings_utm = processing.run("native:reprojectlayer", { 'INPUT': buildings, 'TARGET_CRS': crs_utm })['OUTPUT'] # 2. Filter buildings by area suitable = processing.run("native:extractbyexpression", { 'INPUT': buildings_utm, 'EXPRESSION': '"area_sqm" >= 800 AND "area_sqm" <= 1200' })['OUTPUT'] # 3. Buffer schools 1000m, select within school_zone = processing.run("native:buffer", { 'INPUT': schools, 'DISTANCE': 1000 })['OUTPUT'] result = processing.run("native:extractbylocation", { 'INPUT': suitable, 'PREDICATE': [0], 'INTERSECT': school_zone })['OUTPUT']
QGIS + AI Automation Workshop · github.com/your-repo

## Slide 11
11/15
🏗️ Production Architecture
PyQGIS Script
PostgreSQL + PostGIS
GeoServer WMS / WFS
Leaflet Web Map
✨ Benefits
🔄 Scheduled re-analysis — cron / GitHub Actions
🌐 Web services — REST API, tile caching
👥 User permissions — role-based access
📱 Access from any device — desktop, tablet, phone
QGIS + AI Automation Workshop · github.com/your-repo

## Slide 12
12/15
🌍 Use Cases
🏪 Retail Site Selection
Find optimal store locations based on demographics, competitor proximity, traffic patterns
🏥 Healthcare Facility Placement
Identify underserved areas for clinics, hospitals, and emergency services
🌳 Conservation Reserve Design
Design protected areas using ecological criteria, connectivity, and land use
🚒 Emergency Response Planning
Locate fire stations, evacuation centers, and supply depots for disaster readiness
🏘️ Urban Development Zoning
Evaluate parcels for rezoning, density changes, and mixed-use development
📡 Telecom Tower Placement
Optimize coverage by analyzing terrain, population density, and existing infrastructure
QGIS + AI Automation Workshop · github.com/your-repo

## Slide 13
13/15
💡 Key Takeaways
⚡ QGIS + Python replaces hours of clicking — one command, 25 seconds
🔧 PyQGIS gives you access to 800+ processing algorithms
♻️ Same workflow for ANY site selection problem — retail, conservation, emergency
📈 From local script → PostgreSQL → GeoServer → public web map
💰 100% open source — QGIS, Python, Folium, PostgreSQL — no license fees
🌍 Perfect for low-resource regions where ArcGIS is unaffordable
QGIS + AI Automation Workshop · github.com/your-repo

## Slide 14
14/15
📚 Resources & Next Steps
📄 Download the code:
github.com/saltcotraining-geoai/qgis-ai-site-selection
📺 Watch the demo video:
youtube.com/@Saltco_GeoTraining
📖 QGIS PyQGIS Documentation:
qgis.org/pyqgis
📦 Processing Algorithms Reference:
docs.qgis.org/latest/en/docs/user_manual/processing_algs.html
🐘 PostGIS Documentation:
postgis.net/documentation
🌐 GeoServer:
geoserver.org
📚 Dataset:
QGIS Training Manual (CC-BY-SA) + OpenStreetMap (ODbL)
📺 Subscribe for more QGIS + AI automation workflows
QGIS + AI Automation Workshop · github.com/your-repo

## Slide 15
15/15
Thank You
Questions?
"The best GIS analyst is the one who automates their workflow."